## Slide 1: Data-Quality Rating Script Rates Time-Series Water-Quality Data as Excellent, Good, Fair, Poor, or Consider Deletion
Stewart Rounds USGS Oregon Water Science Center Portland, OR
U.S. Department of the Interior
U.S. Geological Survey
Notes: Slides from internal USGS training on Data-Quality Ratings for Continuous Water-Quality Data.
For questions contact Stewart Rounds or see http://water.usgs.gov/usgs/owq/dqrating/

## Slide 2: Part of the Recommended Workflow
http://water.usgs.gov/usgs/owq/dqrating/

## Slide 3: Data-Quality Ratings – The Details
Grabs edited and computed instantaneous values from NWIS
Grabs unrounded data corrections from tables 1, 2, & 3
Computes data corrections for every data point
  includes rounding methods
  includes “parallel” computations for WY 2002-2006
Compares final corrections to computed data
  recommends running a primary if some level of disagreement
Computes total correction criteria for every data point
  sum of absolute values of data corrections from tables 1, 2, & 3
  sum of absolute values of percentage data corrections
Rates each instantaneous value (excellent, good, fair, poor, consider deletion) using criteria from T&M 1-D3 as well as other criteria
Rates each day (minimum [default] or median rating)
Results not stored in NWIS; can be included in station analysis
http://water.usgs.gov/usgs/owq/dqrating/

## Slide 4: Data-Quality Ratings – Syntax
dq_rating.pl db_name db_num siteID DD bdate edate
where
db_name = name of NWIS database (nwisor in Oregon)
db_num = ADAPS database number (1 in Oregon)
siteID = site ID number
DD = ADAPS data descriptor (DD) number
bdate = begin date for data-quality ratings
edate = end date for data-quality ratings
Dates can be specified in a variety of formats: YYYYMMDD, MM-DD-YYYY, Mon-DD-YYYY, DD-Mon-YYYY and either slashes (/) or dashes (-) can be used as separators
Examples:
dq_rating.pl nwisor 1 14206950 6 20091001 20100930
dq_rating.pl nwisor 1 14206950 6 10/1/2009 9/30/2010
dq_rating.pl nwisor 1 14206950 6 Oct-1-09 Sep-30-10
http://water.usgs.gov/usgs/owq/dqrating/

## Slide 5: Example Rating
pH
daily minimum rating (the default rating type)
100% verification of computed data
shows results in date ranges for qualitative categories
  Excellent
  Good
  Fair
  Poor
  Consider deletion
http://water.usgs.gov/usgs/owq/dqrating/

## Slide 6: Data-Quality Ratings – Optional Syntax
dq_rating.pl db_name db_num siteID DD bdate edate [unit | median] [wDVmean | wDVmed]
where
unit = [optional] flag specifying that ratings be reported for unit values rather than daily ratings based on the minimum unit value rating
median = [optional] flag specifying that daily ratings be based on the median unit value rating for the day rather than the minimum
wDVmean = [optional] flag specifying that ratings be provided only for those dates where a computed daily mean value is available
wDVmed = [optional] flag specifying that ratings be provided only for those dates where a computed daily median value is available
Examples:
dq_rating.pl nwisor 1 14206950 6 20091001 20100930 unit
dq_rating.pl nwisor 1 14206950 6 20091001 20100930 wDVmean
dq_rating.pl nwisor 1 14206950 6 20091001 20100930 median wDVmed
http://water.usgs.gov/usgs/owq/dqrating/

## Slide 7: Example Rating
unit option:
unit-value rating
100% verification of computed data
shows results in date ranges for qualitative categories
  Excellent
  Good
  Fair
  Poor
  Consider deletion
http://water.usgs.gov/usgs/owq/dqrating/

## Slide 8: Example Rating
wDVmed option:
daily minimum rating, only for days when daily median exists
New category:
  Not rated
http://water.usgs.gov/usgs/owq/dqrating/

## Slide 9: Parting Thoughts
This rating capability may or may not be incorporated into the Aquarius software. Wade has incorporated it into wqmreview.
Hopefully, this rating system eventually will be superseded or augmented in Aquarius by a system that computes uncertainty quantitatively for every instantaneous value and every daily value.
Questions can be directed to: Stewart Rounds sarounds@usgs.gov 503-251-3280
http://water.usgs.gov/usgs/owq/dqrating/